## Slide 1: CallPilot 150 Modem Access
Jan 03, 2005
Version 1.5

## Slide 2: CallPilot 150 Remote Access Procedure
CallPilot Small Systems provide a V.34 33.6 kbps analog modem that allows support personnel to perform maintenance actions remotely.
This document provides an overview of how to use this capability. The process involves the following steps:
  Connecting a telephone to your modem
  Setting up Dial-Up Networking on your PC
  Running the Nortel Networks CPsecureModem.exe on your PC
  Logging into a support mailbox on the CallPilot system
  Starting the RAS connection

## Slide 3: Configuring Your PC Connecting a Phone to your Modem
In order to access the CallPilot support modem, you need log-in to a special support mailbox and enter a password.
  This requires listening to voice prompts and entering DTMF digits, which can be done using a telephone that is connected to your modem
External Modem
  Plug your telephone into your modem
  Connect your modem to the telephone line
Internal Modem / PC-Card Modem
  Connect your modem to the telephone line
  Connect your telephone to the telephone line in parallel with the modem connection
    The telephone acts like an extension in this case and shares the telephone line with the modem. You only require a single telephone line to be provided by the telephone company.
    You can purchase a $4 ‘telephone line splitter’ from stores that sell telephones (e.g. Radio Shack, Staples) that you can plug into a phone jack that will allow 2 devices to be plugged into the phone jack in parallel

## Slide 4: Windows 95/98 Step 1: Create A Dial-Up Networking Entry
Select Programs/Accessories/Communications/Dial-Up Networking
Click on ‘Make New Connection’
Enter a Phonebook entry name
Select a modem from the list and click ‘Configure’
  On the Options tab, check ‘Operator assisted or manual dialing’ and click OK
Click Next and enter the telephone number to dial
Click Finish

## Slide 5: Windows 95/98 Step 2: Configure the Dial-Up Networking TCP/IP Parameters
Right-click on the Dial-Up Networking icon created in the previous step and select Properties from the pop-up menu
Click on the Configure button
On the Server Types page:
  For Type of Dial-up server, select PPP: Internet, ….
  Under Advanced Options:
    Check Log on to network
    Uncheck Enable software compression
    Uncheck Require encrypted password
    Uncheck Require data encryption
    Uncheck Record a log file for this connection
  Under Allowed network protocols:
    Ensure TCP/IP is checked
    Click on the TCP/IP settings button
      Select Specify an IP address and enter the IP address 192.168.0.10. This IP address will be used to identify the local PC during the modem session. Configuration of this IP address does not impact the LAN configuration that may also be present on the local PC.
      Un-check ‘Use IP header compression’
      Uncheck ‘Use default gateway on remote network’
Go to the ‘Run CPsecureModem’ slide of this presentation
192. 168 . 0 .10

## Slide 6: Windows NT 4 Step 1: Create A Dial-Up Networking Entry
Select Programs/Accessories/Dial-up Networking from the Start Button menu
Click on the ‘More’ Button
  Select ‘Operator assisted or manual dialing’
Click the ‘New’ button
  Enter a name for the new connection
  Check the ‘I know all about dial up connections and would prefer to edit the properties directly’
  The modem connection properties are then displayed.

## Slide 7: Windows NT 4 Step 2: Configure the Dial-Up Networking TCP/IP Parameters
Click on the ‘Configure’ button
  Select Initial Host speed as 115200
  Check enable hardware flow control
  Uncheck enable modem error control and modem compression
  Click OK
Select the Server page
  For ‘Dial-up server type’, select PPP: Internet…
  Ensure the following checkboxes are checked:
    TCP/IP, Enable software compression, Enable PPP LCP extensions
Click the TCP/IP settings button
  Select 'Use the following IP address‘ and enter the IP address 192.168.0.10. This IP address will be used to identify the local PC during the modem session. Configuration of this IP address does not impact the LAN configuration that may also be present on the local PC.
  Un-check ‘Use IP header compression’
  Uncheck ‘Use default gateway on remote network’
  Click OK.
        Continued…

## Slide 8: Windows NT 4 Step 2: Configure the Dial-Up Networking TCP/IP Parameters (Continued)
Select the Security page
  Check ‘Accept any authentication including clear text’
  Click OK
To change the settings at a later time…
  Select Dial-up Networking from Start/Programs/Accessories
  Click the More button and select ‘Edit Entry and modem properties…’
Go to the ‘Run CPsecureModem’ slide of this presentation

## Slide 9: Windows 2000 Step 1: Create A Dial-Up Networking Entry
Select ‘Network and Dial-up Connections’ from Start/Programs/Accessories/Communications
  Click on ‘Make New Connection
  In the Network Connection Wizard, select ‘Dial-up to the Internet’
In the Internet Connection Wizard dialog box, select ‘I want to set up my Internet Connection Manually …’ and click Next
In the ‘Setting Up your Internet Connection’ dialog box, select ‘I connect through a phone line and a modem’
      Continued…

## Slide 10: Windows 2000 Step 1: Create A Dial-Up Networking Entry (continued)
Internet Account Creation Information
  Enter a phone number (this is not actually used)
  Click the ‘Advanced’ button and select the ‘Address’ page
  In the IP Address box, select ‘Always use the following IP address’ and enter the IP address 192.168.0.10. This IP address will be used to identify the local PC during the modem session. Configuration of this IP address does not impact the LAN configuration that may also be present on the local PC. Click OK and then Next
Internet Account Login Information
  Leave the user name as Administrator and the password field blank
Configuring Your Computer
  Provide a connection name

## Slide 11: Windows 2000 Step 2: Configure the Dial-Up Networking TCP/IP Parameters
Right-click on the Dial-Up Networking icon that you have created and select Properties from the pop-up menu
  Click on the Configure button
    Hardware features: ensure the following items are checked:
      Enable hardware flow control
      Disable modem error control
      Disable modem compression
    Initialization : uncheck the following
      Show Terminal window
      Run Script
    Security: select Advanced (custom settings)
      Settings
        select 'Allow these protocols'
        check only Unencrypted password (PAP)

## Slide 12: Windows 2000 Step 2: Configure the Dial-Up Networking TCP/IP Parameters (Cont’d)
On the Networking Page:
  For Type of dial-up server I am calling: select PPP: Windows 95/98/NT4/2000,Internet
  Click the Settings button:
    Check all PPP settings (LCP extensions, enabled software compression, Negotiate multi-link for single link connections)
  In the ‘Components checked are used by this connection’ box:
    ensure Internet Protocol (TCP/IP) is checked
    Select the Internet Protocol (TCP/IP) item and click 'Properties':
    Select 'Use the following IP address' and and enter the IP address 192.168.0.10. This IP address will be used to identify the local PC during the modem session. Configuration of this IP address does not impact the LAN configuration that may also be present on the local PC.
Go to the ‘Run CPsecureModem’ slide of this presentation

## Slide 13: Windows XP Step 1: Create A Dial-Up Networking Entry
Select ‘New Connection Wizard’ from Start/Programs/Accessories/Communications
  In the New Connection Wizard, select ‘Connect to the network at my workplace” and click Next
In the New Connection Wizard dialog box, select the Network Connection type as ‘Dial-up connections’ and click Next
Continued…

## Slide 14: Windows XP Step 1: Create A Dial-Up Networking Entry (continued)
Configuring Your Connection
  Provide a Connection Name
  Enter a phone number (this is not actually used)
  Make sure you type an number in the phone number field. The connection would fail if the phone number field is left empty.
  Make the new connection Available to any user or only to yourself.

## Slide 15: Windows XP Step 2: Configure the Dial-Up Networking TCP/IP Parameters
Right-click on the Dial-Up Networking icon that you have created and select Properties from the pop-up menu
  Click on the Configure button under the General tab
    Hardware features: ensure the following items are unchecked:
      Enable hardware flow control
      Enable modem error control
      Enable modem compression
    Initialization : uncheck the following
      Show Terminal window
  Click on the Options tab
    Dialing options: select and deselect the following
      select the ‘Display progress while connecting’ and ‘Prompt for name and password,certificate, etc.’
      deselect the ‘Include Windows logon domain’ and ‘Prompt for phone number’

## Slide 16: Windows XP Step 2: Configure the Dial-Up Networking TCP/IP Parameters (Cont’d)
  Click on the Security tab
    Security options: select Advanced (custom settings)
      Click Settings
        select 'Allow these protocols'
        check only Unencrypted password (PAP)

## Slide 17: Windows XP Step 2: Configure the Dial-Up Networking TCP/IP Parameters (Cont’d)
On the Networking Page:
  For Type of dial-up server I am calling: select PPP: Windows 95/98/NT4/2000,Internet
  Click the Settings button:
    Check all PPP settings
      Enable LCP extensions
      Enable software compression
      Enable Negotiate multi-link for single link connections
  In the ‘Components checked are used by this connection’ box:
    ensure Internet Protocol (TCP/IP) is checked
    Select the Internet Protocol (TCP/IP) item and click 'Properties':
    Select 'Use the following IP address' and and enter the IP address 192.168.0.10. This IP address will be used to identify the local PC during the modem session. Configuration of this IP address does not impact the LAN configuration that may also be present on the local PC.
Refer Callpilot 100/150 Installation and Maintenance Guide for use ‘CPsecureModem’

## Slide 18: Run CPsecureModem
CPsecureModem.exe configures your modem so that it can use a special connection mode
  Improves the security of the CallPilot system by making it more difficult for hackers to connect into the system
IMPORTANT: The CPsecureModem configuration must changed back to ‘Normal Operation’ mode before you can use the modem to connect to systems other than CallPilot Small Systems
To change your CPsecureModem configuration:
  Run CPsecureModem
    The current configuration status is displayed in the Status Bar at the bottom of the application window
  Select the option that you want: CP secure access or normal operation
  Click OK. A ‘Configuration Change Complete’ notice will be displayed.
  On Windows NT 4, the Configuration Complete notice will inform you that changes will not take effect until after you have restarted your PC.

## Slide 19: Logging into the CP System
Double click the Dial-Up Networking entry you created to access the CP system
Enable operator-assisted calls or manual dialing ( i.e. Open Dial-Up Networking. On the Advanced menu, click Operator-Assisted Dialing )
Set the User ID to CallPilot
Set the Password to administrator
If there is a field labeled ‘Domain:’, set this to the IP address you entered for the desktop networking client
Click the Connect button
  The dialog box shown below will appear:
Windows XP
Windows 98
Windows NT4 / 2000

## Slide 20: Logging into the CP System (continued)
Using the telephone, dial into the CallPilot system auto-attendant. When prompted, enter ** followed by the support mailbox and number sign (e.g. **12#), and then enter the password.
If the CallPilot system has enough resources to start the modem, it will start counting down from 5. After it says ‘1’, click on the Connect button and hang up the phone. Windows will display when the connection has been established.
  Tip: If the prompt “One moment please” is played the system currently does not have sufficient resources to access the modem. Please wait for the countdown before clicking the connect button.
  Tip: If the prompt “One moment please” is played a number of times followed by “Exiting the system, goodbye”, please try your call again.

## Slide 21: Once The Connection Has Been Established…
When connected to the CallPilot via CPSecureModem the CallPilot will always be referenced using the IP address 192.168.0.2.
Once the modem connection has been successfully established you can test the modem connection using the “ping” application from the local PC.
To test:
  Open a DOS command window from the local PC
  Type ping 192.168.0.2
  You should receive the response “Reply from 192.168.0.2 …”
  If you do not receive this response please refer to the configuration instructions for your particular OS to ensure that the configuration was completed successfully.
To establish a telnet session:
  Click Start / Run…
  Enter Telnet 192.168.0.2 and click OK
To use CallPilot Manager:
  Use the address http://192.168.0.2 in the address field of your web browser